## Slide 1: ECE 382 Lesson 4
Readings
  MSP430 Family Users Guide pp47-55 Davies 5.2 (pp125 - pp131) MSP430 Addressing Modes
Lesson Outline
  Addressing Modes
  CompEx1  due lesson 6
Admin
  Assignment 1 due today
  Assignment 2 due next lesson

## Slide 2: Basic addressing modes
Code | Addressing Mode | Description | Example
00 | Rn | Register direct | mov r5, r6
01 | offset(Rn) | Register indexed | mov 2(r5), r6
10 | @Rn | Register indirect | mov @r5, r6
11 | @Rn+ | Register indirect with post-increment | mov @r5+, r6
r5 | 0200
r6 | 0000
200 | 34
201 | 12
202 | 78
203 | 56
registers
memory

## Slide 3: Basic addressing modes
Code | Addressing Mode | Description | Example
00 | Rn | Register direct | mov r5, r6
01 | offset(Rn) | Register indexed | mov 2(r5), r6
10 | @Rn | Register indirect | mov @r5, r6
11 | @Rn+ | Register indirect with post-increment | mov @r5+, r6
r5 | 0200
r6 | 0200
200 | 34
201 | 12
202 | 78
203 | 56
registers
memory

## Slide 4: Basic addressing modes
Code | Addressing Mode | Description | Example
00 | Rn | Register direct | mov r5, r6
01 | offset(Rn) | Register indexed | mov 2(r5), r6
10 | @Rn | Register indirect | mov @r5, r6
11 | @Rn+ | Register indirect with post-increment | mov @r5+, r6
r5 | 0200
r6 | 0000
200 | 34
201 | 12
202 | 78
203 | 56
registers
memory

## Slide 5: Basic addressing modes
Code | Addressing Mode | Description | Example
00 | Rn | Register direct | mov r5, r6
01 | offset(Rn) | Register indexed | mov 2(r5), r6
10 | @Rn | Register indirect | mov @r5, r6
11 | @Rn+ | Register indirect with post-increment | mov @r5+, r6
r5 | 0200
r6 | 5678
200 | 34
201 | 12
202 | 78
203 | 56
registers
memory
0200
+ 2
0202
How about: mov.w 2(r5), 6(r5) ???

## Slide 6: Basic addressing modes
Code | Addressing Mode | Description | Example
00 | Rn | Register direct | mov r5, r6
01 | offset(Rn) | Register indexed | mov 2(r5), r6
10 | @Rn | Register indirect | mov @r5, r6
11 | @Rn+ | Register indirect with post-increment | mov @r5+, r6
r5 | 0200
r6 | 0000
200 | 34
201 | 12
202 | 78
203 | 56
registers
memory

## Slide 7: Basic addressing modes
Code | Addressing Mode | Description | Example
00 | Rn | Register direct | mov r5, r6
01 | offset(Rn) | Register indexed | mov 2(r5), r6
10 | @Rn | Register indirect | mov @r5, r6
11 | @Rn+ | Register indirect with post-increment | mov @r5+, r6
r5 | 0200
r6 | 1234
200 | 34
201 | 12
202 | 78
203 | 56
registers
memory
Like a pointer
Is this the same as: move 0(r5), r6 ???

## Slide 8: Basic addressing modes
Code | Addressing Mode | Description | Example
00 | Rn | Register direct | mov r5, r6
01 | offset(Rn) | Register indexed | mov 2(r5), r6
10 | @Rn | Register indirect | mov @r5, r6
11 | @Rn+ | Register indirect with post-increment | mov @r5+, r6
r5 | 0200
r6 | 0000
200 | 34
201 | 12
202 | 78
203 | 56
registers
memory

## Slide 9: Basic addressing modes
Code | Addressing Mode | Description | Example
00 | Rn | Register direct | mov r5, r6
01 | offset(Rn) | Register indexed | mov 2(r5), r6
10 | @Rn | Register indirect | mov @r5, r6
11 | @Rn+ | Register indirect with post-increment | mov @r5+, r6
r5 | 0202
r6 | 1234
200 | 34
201 | 12
202 | 78
203 | 56
registers
memory

## Slide 10: Addressing Mode Worksheet
Worksheet
Numbers and Labels?
Other addressing modes:
  Immediate: mov.w #BEEF, r6
  PC Relative: mov.w magic_number, r7
      magic_number .word 0xafaf
      becomes mov.w xxxx(PC), r7
  Absolute: mov.w &0200, r6
    mov.w #0xff, &P1OUT
    move.w #xff, P1OUT ????

## Slide 11: Let's write a MSP430 program
  Our chip version: Msp430g2553  open CCS
; This program sets all pins on Port 1 to output and high. Since LEDs 1 and 2 are connected to P1.0 and P1.6 respectively, they will light up. This program turns the LEDs on and off
.text
; turn off watchdog timer
main:
bis.b #0xFF, &P1DIR ; set port1 direction to output
Turn_on:
bis.b #0xFF, &P1OUT ; turn on leds at port1, bis?
; could of: move ____ , &P1OUT
Turn_off:
bic.b #0xFF, &P1OUT ; turn on leds at port1, bic?
; could of: move ____ , &P1OUT
jmp Turn_on ; loop forever
 what?
Stack pointer?

## Slide 12: Example Program Where’s the BEEF?
; example program to fill memory with BEEF -- what are the addressing modes used?
mov.w #0x200, r5
mov.w #0xBEEF,r6
fill: mov.w r6, 0(r5)
incd r5
cmp.w #0x0400, r5
jne fill
forever: jmp forever
Another way to do this?

## Slide 13: Example Program Where’s the BEEF?
; example program to fill memory with BEEF -- what are the addressing modes used?
mov.w #0x200, r5
mov.w #0xBEEF,r6
fill: mov.w r6, @(r5)+
incd r5
cmp.w #0x0400, r5
jne fill
forever: jmp forever

## Slide 14: Sample Program – predict what happens
repeat:
mov.b #0x75, r10
add.b #0xC7, r10
;result should be 0x13c, so we should see 3c in r10 and carry bit set
adc r10
;since carry bit was set, this should increment r10 to 3d
inv.b r10
;invert, so r10 should be c2
mov.w #0x00aa, r10
sxt r10
;sign extend should clear upper 8 bits
inv r10
swpb r10
mov.w r10, r9
jmp repeat
c010: 7a 40 75 00 mov.b #117, r10 ;#0x0075
c014: 7a 50 c7 00 add.b #199, r10 ;#0x00c7
c018: 0a 63 adc r10
c01a: 7a e3 xor.b #-1, r10 ;r3 As==11
c01c: 3a 40 aa 00 mov #170, r10 ;#0x00aa
c020: 8a 11 sxt r10
c022: 3a e3 inv r10
c024: 8a 10 swpb r10
c026: 09 4a mov r10, r9
c028: f3 3f jmp $-24 ;abs 0xc010

## Slide 15: In class programming exercise
; write an example program to add the numbers 10+9+8+...+1

## Slide 16: In class programming exercise
; example program to add the numbers 10+9+8+...+1
mov.w #10, r6
mov.w #0, r5
summation: add.w r6, r5
dec r6
jnz summation
mov.w r5, &0x0200
forever: jmp forever

## Slide 17: MSP430’s ISA
Msp430g2553 Memory Map
512b of RAM - 0x200-0x400 16kb of ROM - 0xc000-0xffdf
0x1100-0xc000 is empty!
- There is no memory backing it up!
- If you attempt to write to this area of memory, you'll trigger what's essentially a segmentation fault because that memory doesn't exist. It will cause the chip to do a Power-up Clear (PUC), resetting the state of your processor. This is a tough error to debug.
How many addr bits?

## Slide 18: Assembly and Machine Languages
Instructions:
  words in a computers language
Instruction Set:
  the dictionary of the language
Assembly Language:
  human-readable format of computer instructions
Machine Language:
  computer-readable instructions - binary (1's and 0's)
Assembler
Assembly Language Program
Linker
Relocatable Object Code
Executable Code