## Slide 1: ECE 382 Lesson 7
Lesson Outline
  Found errors in PWM Assembly Code?
  Instruction Execution Time
  More Assembly Process
  Assembler Directives
  Structured Design and Test
  Lab Guidance
  Lab 1 Introduction
  Assignment 3
Admin
  Assignment 3 (due lesson 8)

## Slide 2: Find the errors in this program
http://ecse.bd.psu.edu/cmpen352/lecture/lecture05.html
http://ecse.bd.psu.edu/cmpen352/lecture/code/badlec5.asm
; intention was to have it generate a PWM waveform on the P1.0 pin attached
duty = 0x20;
while(1) {
cnt = 0x40;
P1.0 = 1;
while (cnt>duty)
cnt-=1;
P1.0 = 0;
while (cnt>0)
cnt-=1;
if (P1.3 == 0) {
while (P1.3 == 0);
duty += 0x08;
duty &= 0x3F;
} }

## Slide 3: Instruction Execution Time
Clock is roughly 1 MHz
  What is the Clock Period?
So how long does this block of code take to execute?
  mov #0x0200, r5
  mov #0xbeef, 0(r5)
  forever jmp forever
Single Operand
  page 60 of TI MSP 430 User’s Manual
Two Operand
  page 61 of TI MSP 430 User’s Manual
Jumps
  All take 2 Cycles

## Slide 4: Watchdog Timer
page 341-347 of TI MSP 430 User’s Manual
If not disarmed, How long to reset?
  It counts 32768 clock cycles, then resets

## Slide 5: Assembler Directives
.cdecls C,LIST,"msp430.h"
.text ;put code in the text section - maps to FLASH (ROM)
StopWDT mov.w #WDTPW|WDTHOLD
.data ;put code into the data section - maps to RAM
.sect ".reset" ;put this at the reset vector
.sect .stack ;make this the location of the stack
MY_RESULTS: .space 20 ; reserves 20 bytes
-----------------
To use:
mov #MY_RESULTS, r5 ; pointer address into r5
mov #0xfefe, &MY_RESULT ; put fefe into 1st two bytes

## Slide 6: Assembler Directives
; Can initialize ROM; cannot initialize RAM
;initialize sequence of bytes
bytes: .byte 9,8,7,6,5,4,3,2,1
;initialize sequence of words
words: .word 0x1111,0x2222,0x3333,0x4444
;initialize strings
myStr: .string "hello, world!"
;initialize characters
Chars: .char 'a','b','c','d‘
; see in CCS

## Slide 7: Assembler Directives
; .equ  assign a label to a particular value
SEVENTEEN: .equ 0x11
;align a variable with a particular multiple of bytes (useful to ensure word on even address)
.align 2
;probably won't use these often, but they're available
.float ;floating point value
.int ;16-bit int
.short ;16-bit int
.long ;32-bit int

## Slide 8: Structured Design and Test
Guiding Principle: Get one small thing working
  Don't write the entire program in one go, then press go, and hope it works. When the entire program is the space you're looking for a bug, it makes debugging really hard.
Modularity
  Modularity is the practice of breaking down a larger program into smaller tasks.
  Makes code more reusable
  Makes code more readable
  Make individual taks more manageable
    Focus on simpler tasks
    Tough to hold a big problem in your brain

## Slide 9
Example Design
Concurrent Processes
Init
Got msg?
Yes
No
Init
Send Msg
Init
Send Ack
Init
Write
Image
Init
Do math
Got Ack?
No
Yes
Msg#1
Ack#1
Process image
New image?
Yes
No
Read Image
New = 1
Read data
FIFO
Write data
New data?
Yes
No
Done?
No
Yes
Do math
Done?
No
Yes
Do math
locked?
Lock
locked?
count++
Data#2
Data#2
Locked?
Locked?
Lock
Lock
Lock
No
No
Yes
Yes
Write Data
Write D
Read D
Read Data
Done?
Done?
No
Yes
Yes
No
Process#1
Process#2
Process#3
Process#4
Memory
Memory
New = 1
image
image
count
count--
New = 0
unlock
unlock

## Slide 10: Testing
How do we know when we're done with a task? Testing!
  You should specify the tests you'll run on the code you're going to write in advance of writing the code. It's a little more work up front, but will save you time debugging down the road.
Write tests that cover all cases - particularly edge cases.

## Slide 11: Lab Notebook Expectations
Lab Noteboook Standards
Things people usually mess up:
  Not testing
  Testing after demonstration
  No hardware design
  Poorly written / commented code
  Post-filling notebooks (or GITHub)

## Slide 12: Assembly Code Style Guidelines
Comments
  Assume the reader is a competent assembly language programmer
  Comment above blocks of code to convey purpose
  Only comment individual lines when purpose is unclear
Labels
  Descriptive!
    loop or loop1 or l1 or blah - not acceptable!
Constants
  Use .equ syntax for all constants!
  Don't want to see naked values

## Slide 13: Assembly Code Style Guidelines
Instruction Choice
  Use the instruction that makes your code readable!
    JHS rather than JC
    INCD rather than ADD #2
  Well-written code requires few comments
Spacing
  Align your code to make it readable
  Put whitespace between logical blocks of code

## Slide 14: Example Code
What is good and bad about this code?
  http://ece382.com/notes/L8/hw_sample.html

## Slide 15: Lab 1 Introduction
The goal of this lab is to implement a simple calculator using assembly language.
Lab 1
How This Lesson Applies
Use assembler directives:
  .byte to put your test program into memory
  .space to reserve space for your results
    Where is this going to go?
Labels for your program / results
.equ for key constants
Modularity
  Section to store results of ops
  Section for each op
Testing
  Specify multiple testing sequences at the beginning!
  I'll test your code with a few of my own

## Slide 16: MSP430’s ISA
Msp430g2553 Memory Map
512b of RAM - 0x200-0x400 16kb of ROM - 0xc000-0xffdf
0x1100-0xc000 is empty!
- There is no memory backing it up!
- If you attempt to write to this area of memory, you'll trigger what's essentially a segmentation fault because that memory doesn't exist. It will cause the chip to do a Power-up Clear (PUC), resetting the state of your processor. This is a tough error to debug.
How many addr bits?

## Slide 17: Assembly and Machine Languages
Instructions:
  words in a computers language
Instruction Set:
  the dictionary of the language
Assembly Language:
  human-readable format of computer instructions
Machine Language:
  computer-readable instructions - binary (1's and 0's)
Assembler
Assembly Language Program
Linker
Relocatable Object Code
Executable Code

## Slide 18: Let's write a MSP430 program
  Our chip version: Msp430g2553  open CCS
; This program sets all pins on Port 1 to output and high. Since LEDs 1 and 2 are connected to P1.0 and P1.6 respectively, they will light up. This program turns the LEDs on and off
.text
; turn off watchdog timer
main:
bis.b #0xFF, &P1DIR ; set port1 direction to output
Turn_on:
bis.b #0xFF, &P1OUT ; turn on leds at port1, bis?
; could of: move ____ , &P1OUT
Turn_off:
bic.b #0xFF, &P1OUT ; turn on leds at port1, bic?
; could of: move ____ , &P1OUT
jmp Turn_on ; loop forever
 what?
Stack pointer?

## Slide 19: Status register and Jumps
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Reserved |  |  |  |  |  |  | V | SCG1 | SCG0 | OSCOFF | CPUOFF | GIE | N | Z | C
Condition Code | Assembly Instruction | Description
000 | JNE/JNZ | Jump if Z==0 (if !=)
001 | JEQ/JZ | Jump if Z==1 (if ==)
010 | JNC/JLO | Jump if C==0 (if unsigned <)
011 | JC/JHS | Jump if C==1 (if unsigned >)
100 | JN | Jump if N==1 - Note there is no jump if N==0
101 | JGE | Jump if N==V (if signed >=)
110 | JL | Jump if N!=V (if signed <)
111 | JMP | Jump unconditionally